## Slide 1: Road Safety Index
By
Sai Raghunath Kolusu
Saint Peter’s University

## Slide 2: IDEA
STATE OF THE ART : Factors affecting the road accidents and safety measures to be implemented.
WHAT IS MISSING : A metric which judges the safety of the route has not been implemented.
PROPOSED SOLUTION : Road Safety Index for a route as a function of Accident Density and weighted mean of indicators is calculated using Principal Component Analysis.

## Slide 3: DATA
Data Source : National Highway Traffic Safety Administration
Data Source URL : http://www-fars.nhtsa.dot.gov
State : Massachusetts
Day of Week | Latitude | Longitude | Fatalities | Injuries | Age | Sex of Driver | DUI | CrashType | 
5 | 32.14201 | -85.7585 | 1 | 4 | 68 | 1 | 1 | 1 | 
1 | 31.43981 | -85.5103 | 1 | 4 | 49 | 1 | 0 | 7 | 
4 | 31.31933 | -85.5151 | 1 | 2 | 20 | 2 | 1 | 1 | 

## Slide 4
User Input for Route
Alternate routes & points extracted using JavaScript
Accident Data subset from points
Accident Data subset at time t
RSI
Accident Density at time t
Weighted mean of indicators at time t
Merge based on Street name and Time
Reading Accident Dataset
Cleaning Dataset for null values
Merge
Reading Traffic Volume Dataset
Cleaning Dataset for null values
Mean Traffic Volume at each hour
Sum
f(accidents, mean volume)t
Normalization
Principal Component Analysis
METHOD & CODE

## Slide 5: RESULTS & VALIDATION
Route | Road Safety Index
Route 1 | 0.172
Route 2 | 0.223
Route 3 | 0.179
The above results can be validated by calculating the number of Accidents.
Route | Number of Accidents
Route 1 | 108
Route 2 | 195
Route 3 | 142

## Slide 6
Transcript
Notes: Good Morning Everyone, I am Sai, It’s my pleasure to present in a deemed organization like Liberty Mutual.
My presentation is related to Road Safety Index calculation for different routes in Boston
There are lot many studies in today’s market describing the influence of various indicators on the Road Accidents but a concrete metric which judges the safety of the route has not been implemented. My project tried to address that issue and calculate a Road Safety Index as a function of Accident Density and weighted mean of indicators using Principal Component Analysis.
I have used data from National Highway Traffic Safety Administration
I have designed code using HTML/Javascript and R.
I extracted the route points along the route, subsetted that with the accident data , merged with Traffic Volume Dataset and calculated the RSI using Principal Component Analysis
I have found out the RSI for the 3 routes and the Route 1 seems to be safer. This can be validated calculating the number of accidents in that route

## Slide 7: Final Slide
Thank you very much, Professor, but I will not be able to make it.